## Slide 1
Single-Cycle 32-bit RISC-V (RV32I) Processor Core
Microarchitectural Block Diagrams, Datapath Derivation & Hardware Architecture
Target FPGA: AMD Xilinx Artix-7 (XC7A35T-1CPG236C, Digilent Basys 3) | Tool: Vivado 2025.2 Course: E3: 245 Processor System Design (DESE, IISc Bangalore) Author: Anirudh Chaturvedi

## Slide 2
Level-0 Top-Level System Architecture (basys3_top)
FPGA Board Integration, Dual-Rate Synchronous Clocking & Peripheral Telemetry
Clock Divider & Synchronizer (clk_100mhz -> clk_cpu)
• Input: 100 MHz Oscillator (W5) • sw[1] = 0: 10 MHz Fast Execution • sw[1] = 1: 1 Hz Visual Single-Step • btnC: Master Active-High Reset
Single-Cycle RV32I CPU Core (rv32i_cpu)
• Datapath & Control (CPI = 1.0) • 32 x 32-bit Register File (Hardwired x0 = 0) • 32-bit ALU (10 Operations) • Immediate Generator (I, S, B, U, J) • Pure Distributed RAM (512x32 = 2048 Bytes) • Unaligned Hardware Memory Transfer Engine • Zero Block RAM (0 BRAM Tiles) • Zero Register Inflation (64x RAM256X1S)
7-Segment Display Driver
• 4-Digit Time Multiplexed • sw[0] = 0: Quotient (14 / 0014) • sw[0] = 1: Remainder (2 / 0002) • Shadow Write-Spy Registers (0 extra read ports!)
LED Status Telemetry
• led[13:0] : PC[15:2] Execution Monitor • led[14] : CPU Clock Heartbeat • led[15] : CPU Self-Halt Indicator (PC = 0x3C)

## Slide 3
Level-1 Detailed Single-Cycle Datapath Organization
Combinational Loop: Fetch -> Decode -> Execute -> Memory -> Writeback (T_crit = 14.19 ns)
Program Counter
(PC Reg [31:0])
Instruction Memory
512 x 32
(Distributed RAM)
Control Unit
Opcode / funct3/7
Combinational
Register File
32 x 32-bit
Dual Async Read
Sync Write
(x0 == 0)
Immediate Gen
I, S, B, U, J
Sign Extender
32-bit ALU
10 Operations
Carry Chains
Result & Zero
Data Mem Unit
4 Banked RAMs
(4 x 512x8)
Unaligned Barrel Shifter
Write-Spy Registers
WB Mux
0: ALU
1: Mem
2: PC+4
3: LUI

## Slide 4
Module 1 Focus: 32-bit RV32I ALU Architecture (alu.v)
10 Base RV32I Operations, Corner-Case Handling, and Hardware Delay Characteristics
ALU Interface & Hardware Implementation
• Inputs: - a[31:0] : Operand A (from Register File rdata1) - b[31:0] : Operand B (from ALUSrc Mux: rdata2 or Imm) - alu_op[3:0] : 4-bit Operation Control • Outputs: - result[31:0] : 32-bit Arithmetic/Logic Result - zero : Asserted when result == 0 (Branch evaluator) • Physical Hardware Mapping: - Maps to 32-bit Fast Carry Chains (CARRY4 primitives) - 128 Slice LUTs on Xilinx Artix-7 - Propagation Delay: T_ALU = 3.45 ns (Part of Critical Path)
Key RTL Insights & Interview Defense Traps
1. 5-bit Shift Window b[4:0]: In a 32-bit processor, shifting >= 32 bits clears the word. 2^5 = 32, so RISC-V specifies only the lower 5 bits b[4:0] control shifts (SLL, SRL, SRA). Ignoring upper 27 bits saves massive LUT muxes! 2. Signed vs. Unsigned Set Less Than (SLT vs. SLTU): - A = 0xFFFFFFFF (-1 signed, 4.29B unsigned), B = 0x00000001 (+1) - SLT : ($signed(a) < $signed(b)) ? 1 : 0 ==> Returns 1 (True) - SLTU : (a < b) ? 1 : 0 ==> Returns 0 (False) 3. Logical vs. Arithmetic Shift (SRL vs. SRA): - SRA preserves the sign bit: $signed(a) >>> b[4:0] - SRL shifts in zeros: a >> b[4:0]

## Slide 5
Memory Architecture & Core PPA Optimization Milestones
Pure Distributed RAM, 16k FF Inflation Resolution, and Unaligned Barrel-Shifting
PPA Optimization #1: Memory Banking
• The 16,384 Flip-Flop Inflation Disaster: - Naive memory was declared as flat array: reg [7:0] mem [0:2047] - Variable unaligned read taps forced Vivado to infer discrete registers - Synthesis time blew up to 25 minutes, consuming 39.4% of the FPGA registers! • The Architectural Solution: - Partitioned into 4 byte-wide Distributed RAM banks (dmem0..dmem3) - Exactly 1 read and 1 write port per bank - Inferred 64 x RAM256X1S primitives directly in SLICEM LUTs - Memory FFs dropped from 16,384 to 0 (256 LUTs total!) - Synthesis time dropped from 25 min to 18 seconds (83x speedup!)
PPA Optimization #2: Unaligned Transfer & Write Spies
• Unaligned Load Dataflow: - Reads Word_0 and Word_1 combinationally - 64-bit continuous span: { Word_1, Word_0 } - Barrel-shifts right by (8 * addr[1:0]) bits - Sign/zero-extended based on funct3 (lb, lh, lw) • Unaligned Store Dataflow: - Base byte mask (sb: 0001, sh: 0011, sw: 1111) - Shifted left by byte offset k = addr[1:0] - [3:0] writes Word_A, [7:4] writes Word_B • Zero-Overhead Write-Spy Debug Registers: - Spies on memory write bus at 0x200 (Quotient) & 0x204 (Remainder) - Avoids adding extra read ports to RAM (which would double LUT RAMs)